# ER-2 Doppler Radar (EDOP) Specifications

| TRANSMITTER |  |
| --- | --- |
| Operating Frequency | 9.6 GHz |
| Wavelength | 3.12 cm |
| Peak Transmit Power | 20 kW |
| Pulse Width (variable 0.25 - 3.0 µs) | 0.5 µs |
| Duty Cycle | 0.01 max. |
| PRF (variable 0.5 – 10 kHz) | 4400 kHz (dual-PRF) |
| LO Frequency | 10 MHz |
| RECEIVER |  |
| IF Frequency | 60 MHz |
| Dynamic Range (with dual nadir channel) | 80 (>100) dB |
| Minimum Detectable Signal at 1 km and 10 km range (0.5 µs PW) (w/o addit. averaging) | -25dBZ (-5 dBZ) |
| Number of Channels | 4 |
| PROCESSOR & RADAR CONTROLLER |  |
| Digital Receiver (NCAR VIRAQ/QUAD) | 4 |
| Digital Signal Processor (TI TMS320C44) | 6/channel |
| Host Computer (Motorola) | MVME-167 |
| Computer Bus | VME |
| Operating System | VxWorks |
| Navigation Data | Serial INS/GPS (1 Hz), ARINC 429 (8Hz), P-Code GPS (5 Hz) |
| Parameters: | Zvv, Vvv, vv LDR (nadir-rain) Zvv, Vvv, vv (nadir-surface) Zvv, Vvv, vv (forward co-pol.) Zvh, Vvh, vh (forward crs. pol.) |
| Number of range gates | 720/channel |
| Range resolution (variable 25 m – 300 m) | 37.5 m |
| Averaging interval (variable) | 0.5 s |
| ANTENNA |  |
| Transmit/Receive Polarization States | V |
| Antenna Diameter (Beamwidth) | 0.76 m (2.9o) |
| Antenna Gain | 36 dB |
| Cross-Polarization Isolation | <35 dB (<27 dB installed) |